## Slide 1: Experiment 3 summary
Alexandre Fieno
Electrical Engineering, Mathematics and Computer Science Department - EEMCS

## Slide 2
Video quality
Understand the influence of a set of artifacts on the quality of video, and their relationship with the content
ITU-Recommendation BT.500
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment

## Slide 3
Database of 140 videos sequences
  Generated from 7 high-definition videos (original videos)
  1280 x 720, 50 fps and 10 seconds duration
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment

## Slide 4
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
Combination | Packet Loss | Blocky | Blurry
1 | 0.0 | 0.0 | 0.0
2 | 0.0 | 0.6 | 0.0
3 | 0.0 | 0.0 | 0.6
4 | 8.1 | 0.0 | 0.0
5 | 0.7 | 0.0 | 0.4
6 | 8.1 | 0.0 | 0.4
7 | 0.7 | 0.0 | 0.6
8 | 8.1 | 0.0 | 0.6
9 | 0.7 | 0.4 | 0.0
10 | 8.1 | 0.4 | 0.0
11 | 0.7 | 0.4 | 0.4
12 | 8.1 | 0.4 | 0.4
13 | 0.7 | 0.4 | 0.6
14 | 8.1 | 0.4 | 0.6
15 | 0.7 | 0.6 | 0.0
16 | 8.1 | 0.6 | 0.0
17 | 0.7 | 0.6 | 0.4
18 | 8.1 | 0.6 | 0.4
19 | 0.7 | 0.6 | 0.6
20 | 8.1 | 0.6 | 0.6
Artefacts
  Packet Loss, blockiness and blurriness
  These artefacts can be considered among the most relevant for digital video applications
  Blockiness and blurriness strengths and, packet loss ratios have been used in previous experiments

## Slide 5
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
For each test sequence
  MOS (mean opinion score)
  Standard deviation
ANOVA
T-Test

## Slide 6
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
Blockiness, blurriness and packet loss artefacts, for the same video:
  Park Joy: there were a statistically significant difference between artefacts as determined by one-way ANOVA (F(2,66)=4.730, p<0.05).
  A T-Test revealed that had statically significant difference between blockiness (M=51.96) and blurriness ((M=32.74), t(44)=2.015, p=0.005) artefacts and, between blockiness (M=51.96) and packet loss ((M=38.70), t(44)=2.105, p=0.019) artefacts.
  There were no statistically significant differences between the blurriness (M=32.74) and packet loss (M=38.70) artefacts, where p=0.412.

## Slide 7
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
Blockiness, blurriness and packet loss artefacts, for the same video:
  Park Run: there were a statistically significant difference between artefacts as determined by one-way ANOVA (F(2,66)=19.959, p<0.05).
  A T-Test revealed that had statically significant difference between blurriness (M=58.08) and packet loss ((M=20.52) (t(44)=2.015, p=0.000) artefacts and, between blockiness (M=53.35) and packet loss ((M=20.52), (t(44)=2.105, p=0.000) artefacts.
  There were no statistically significant differences between the blurriness (M=58.08) and blockiness (M=53.35) artefacts, where p=0.494.

## Slide 8
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
Blockiness, blurriness and packet loss artefacts, for the same video:
  Romeo and Juliet: there were a statistically significant difference between artefacts as determined by one-way ANOVA (F(2,66)=16.979, p<0.05).
  A T-Test revealed that had statically significant difference between blurriness (M=12.74) and blockiness ((M=45.56), t(44)=2.015, p=0.000) artefacts and, between blurriness (M=12.74) and packet loss ((M=43.96), t(44)=2.105, p=0.000) artefacts.
  There were no statistically significant differences between the blockiness (M=45.56) and packet loss (M=43.96) artefacts, where p=0.808.

## Slide 9
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
Blockiness, blurriness and packet loss artefacts, for the same video:
  Barbecue: there were a statistically significant difference between artefacts as determined by one-way ANOVA (F(2,66)=14.997, p<0.05).
  A T-Test revealed that had statically significant difference between blurriness (M=25.26) and blockiness ((M=60.60), t(44)=2.015, p=0.000) artefacts, between blurriness (M=25.26) and packet loss ((M=41.86), t(44)=2.105, p=0.025) artefacts and, between blockiness (M=60.60) and packet loss ((M=41.86), t(44)=2.105, p=0.000) artefacts.

## Slide 10
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
Blockiness, blurriness and packet loss artefacts, for the same video:
  Into Tree: there were no a statistically significant difference between artefacts as determined by one-way ANOVA (F(2,66) = 0.888, p=0.416)
  Cactus: there were no a statistically significant difference between artefacts as determined by one-way ANOVA (F(2,66) = 1.043, p=0.358)
  Basketball: there were no a statistically significant difference between artefacts as determined by one-way ANOVA (F(2,66) = 3.104, p=0.051)

## Slide 11
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
Blurriness artefact, for different videos:
  Blurriness: There were a statistically significant difference between videos sequences as determined by one-way ANOVA (F(6,154)=6.851, p<0.05)
Videos | N | Mean | St. Deviation
Park Joy | 23 | 32.74 | 27.00
Into Tree | 23 | 39.70 | 29.55
Park Run | 23 | 58.09 | 26.44
Romeo & Juliet | 23 | 12.74 | 19.87
Cactus | 23 | 26.52 | 21.14
Basketball | 23 | 32.13 | 29.01
Barbecue | 23 | 25.26 | 25.64

## Slide 12
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
Blockiness artefact, for different videos:
  Blockiness: There were a statistically significant difference between videos sequences as determined by one-way ANOVA (F(6,154)=4.597, p<0.05)
Videos | N | Mean | St. Deviation
Park Joy | 23 | 51.96 | 14.81
Into Tree | 23 | 44.43 | 18.43
Park Run | 23 | 53.35 | 19.69
Romeo & Juliet | 23 | 45.57 | 19.27
Cactus | 23 | 34.61 | 20.34
Basketball | 23 | 49.52 | 19.11
Barbecue | 23 | 60.61 | 15.64

## Slide 13
Electrical Engineering, Mathematics and Computer Science Department - EEMCS
Experiment
Packet loss artefact, for different videos:
  Packet Loss: There were a statistically significant difference between videos sequences as determined by one-way ANOVA (F(6,154)=4.696, p<0.05)
Videos | N | Mean | St. Deviation
Park Joy | 23 | 38.70 | 21.52
Into Tree | 23 | 49.52 | 25.73
Park Run | 23 | 20.52 | 18.97
Romeo & Juliet | 23 | 43.96 | 25.01
Cactus | 23 | 27.78 | 19.77
Basketball | 23 | 43.57 | 23.02
Barbecue | 23 | 41.87 | 23.17