## Slide 1: International conference on circuits and systems - iscas 2013 On the impact of packet-loss impairments on visual attention mechanisms Judith A. Redi, Ingrid Heynderickx, Bruno Machiavello and Mylene Farias

## Slide 2: Overview
Packet Loss Artifacts, visual annoyance and impact on Quality of Experience (QoE)
Visual attention and its impact on QoE
The role of visual attention in the annoyance of Packet Loss Artifacts
  A subjective experiment involving eye-tracking
  Data analysis and results
Conclusions and future research

## Slide 3: Packet loss artifacts
H.264/AVC: (compressed) video information is encapsulated in NAL packets
Network errors  lost packets  error concealment
Loss in visual quality and overall QoE (e.g., Staelens 2012)
What can we do about it?
Notes: You are probably familiar with h264 avc
What it does is that it encapsulates coded video info into a network abstraction level, so each frame is divided into slices that are then encapsulated into packets, that might get lost

## Slide 4: Visual attention and qoE
The HVS minimizes the amount of visual information to process by focusing on peculiar, more informative regions, (a.k.a, salient regions)
Notes: But we were not yet fully happy so we started looking deeply in features of the HSV to better estimate quality. What we found is that visual attention could have been useful to our purposes. Your brain bla bla
Thus the idea is that if some areas are less visible than others, you can also imagine tat distortions in those areas will be less visible. This has a number of implications. First of all for the objective computation
Then for the signal optimization and enhancement, iin view of computational cost saving you can drive most of the algorithm actions in the ROI

## Slide 5: visual attention and QoE
Artifacts in the most salient regions are more annoying than those in the background (Alers 2010, Engelke 2011)
This can be modeled into objective metrics (Liu 2010)
  With mixed results for video (Le Meur 2012)
Distortion map
NSS
original
distorted
Quality Measure
What happens to saliency with packet loss artifacts, which are sudden and strongly localized?
Can packet loss artifacts distract attention?
Eye-tracking study

## Slide 6: Eye-tracking study setup: stimuli
Original
720p, CVDL
h.264 encoding
PSNR>70db, 120 Mbps
GOP = 4, 8, 12
Network error simulation
Loss Ratio = 0.7%, 2.6%, 4.3% , 8.1%

## Slide 7: Eye-tracking study setup: protocol
4. How annoying were they?
1. calibration
2. Task free pristine videos
3. Training
4. Scoring task (91 videos)
15 observers
Single Stimulus setup (ITU BT.500)
1. First video view
2. Second video view
3. “did you see imparments?”
Yes/no
0 100

## Slide 8: Analysis of the viewing behavior: saliency
SALIENCY MAP
visual representations of the probability that a location of the scene is attended by the average observer
?
Eye-movements
Fixation Map
400 ms
Frame fixation Map

## Slide 9: Analyzing saliency to understand differences in viewing behavior
Videos divided into 3 groups
 | videos | task | #Videos
FL G1 | pristine | Free Looking | 7
SC HQ | pristine | Scoring | 7
SC LQ | impaired | Scoring | 84
FL G2 | pristine | Free Looking | 7
UESL
SC_FL
SCHQ_SCLQ
Upper Empirical Similarity Limit: human-human consistency
Similarity measure S{LCC, SSIM}

## Slide 10: Results - LCC
If the shift in saliency was due to task, we would expect SCHQ _ SCLQ (red squares) to be closer to the UESL (green triangle) than to the SC_FL values (blue circles). That’s not the case.
Increasing mean annoyance value

## Slide 11: RESULTS - SSIM

## Slide 12: Impact of packet loss and annoyance on eye movements
MAV = Mean Annoyance Value

## Slide 13: conclusions
Packet loss distracts attention
Shift in attention seems to be related to the annoyance provoked by the artifacts, not to the objective parameters describing the artifacts
Further work is needed towards:
  Analysing the shifts in saliency from a spatial point of view (what is becoming more salient in presence of artifacts?)
  Incorporating these results into quality metrics

## Slide 14: Thank you. Questions?
j.a.redi@tudelft.nl

## Slide 15: Video properties

## Slide 16: Analysis of fixations
 |  | Impairment characteristics |  | Video characteristics | 
 |  | GOP_size | P_loss | SI | TI
Diff_fd | Correlation | .215* | .229* | -.334** | -.600**
 | significance | .041 | .029 | .001 | .000

## Slide 17: Saliency data
Saliency map was built by applying to each fixation point a gray-scale patch with Gaussian intensity distribution
  σ ~2° visual angle
k[1, WI], l[1, HI]
iView X RED, SensoMotoric Instruments
sampling rate: 50 Hz
spatial resolution: 0.1
gaze position accuracy: 0.5°-1.0°
Judith Alice Redi Genoa, April 23rd 2010 PhD Defense